## Slide 1
Madelyn Sloan Berry, Daniel Hurley, Elijah Frazure, & Mims Hillis
Mississippi State University
AIAA Region II Student Conference, April 2nd-5th 2025
Copyright © by Madelyn Sloan Berry, Daniel Hurley, Elijah Frazure, Mims Hillis Published by the American Institute of Aeronautics and Astronautics, Inc., with permission.
Utilization of a Portable Ground Station to
Conduct Site Surveys in the S-Band
Frequency for CubeSat at MSU’s Mission

## Slide 2: Mission and Purpose for Conducting Site Surveys
CubeSat at MSU
  Undergraduate team working to design, launch, and operate Mississippi’s first satellite: 1-Mississippi
Hyperspectral Imaging Payload
  S-Band Frequency (2.4 GHz)
Ground Station Communication System Development

## Slide 3: Experiment and Project Outline
Test Ground Station Development
Conducting Site Surveys
Results
Analysis and Conclusion
Where are we going to put our ground station?
  Conducting Site Surveys with a portable test ground station

## Slide 4: Establishing Driving Engineering Factors
Radio Frequency Capabilities
Azimuth & Elevation Control
Portable
Low Cost
System Requirements
Design Constraints

## Slide 5: Overview of Portable Ground Station Design

## Slide 6: User Interface Workstation System Components
Mouse
Monitor
(SDR++)
Keyboard

## Slide 7: Ground Station Interface (GSI) Components
Raspberry Pi 4
Yaesu G-5500 Controller
Caribou Lite
Arduino Uno
Custom 8 Pin Connector

## Slide 8: Antenna Stand System Components
S-Band Antenna
L-Band Antenna
Rotator
Counter Weights
Boom Arm
PA Stand

## Slide 9: Determined Locations to Conduct Site Surveys
North Farm
Walker Roof
Pump House
South Farm
Patterson Lawn
Location criteria
  Accessibility
  Infrastructure
  Regulations
  Safety
  Space

## Slide 10: Establishing Testing Criteria and Scope
Qualitative Data
  Line of Sight (LOS)
  Terrain Description
  Power/Internet Accessibility
Quantitative Data
  Elevation
  Radio Frequency (RF) Analysis
    Noise Level measurements

## Slide 11: Radio Frequency Testing Procedure and Sample Results
Walker Roof (North to South Data) |  | 
Elevation (degrees) | Ground Station (dBW) | Spectrum Analyzer (dBW)
0 | -100 | -120.0
22.5 | -100 | -120.9
45 | -99 | -121.0
67.5 | -98 | -119.9
90 | -98 | -120.4
112.5 | -98 | -120.1
135 | -98 | -120.5
157.5 | -98 | -119.5
180 | -98 | -121.0
Average | -98.56 | -120.37
Measured
Noise Level
Frequency Level
Noise/Background Signals

## Slide 12: Observations From Walker Roof Testing
Excellent Infrastructure
  Aerospace Building
  Power and Internet
  Indoor Storage
RF Environment (Hilbun Hall)
  Noise Floor Increase
  Negligible Impact
    10 degrees Elevation
    5 degrees Azimuth
Walker Roof
Hilbun Hall

## Slide 13: Observations From South Farm Testing
Limited Infrastructure
  Limited Gate Access
  Available Power
  No Indoor Storage
RF Environment
  Expected to be quiet
South Farm
Observatory

## Slide 14: Observations From North Farm Testing
No Infrastructure
  Limited Gate Access
  No available power
  No Indoor Storage
RF Environment
  Expected to be quiet
North Farm

## Slide 15: Observations From Patterson Lab Testing
Limited Infrastructure
  Tall Buildings
  Available Power and Storage
  Limited Space
RF Environment
  Hilbun Interference
  Passing Cars
Patterson Lab

## Slide 16: Observations From Pump House Testing
Limited Infrastructure
  Limited Space
  Available power
  No Indoor Storage
RF Environment
  Passing Cars
Pump House

## Slide 17: Plotting of Collected Noise Data Points

## Slide 18: Comparing Maximum and Minimum Average Noise
Site | Portable Ground Station (dB) | TinySA Spectrum Analyzer (dB)
Walker Roof | -98.28 | -120.37
Patterson Lawn | -99.67 | -119.89
Pump House | -99.78 | -120.20
North Farm | -100.06 | -119.89
South Farm | -100.44 | -119.99
Ground Station Range: 2.17 dB
TinySA Range: 0.48 dB

## Slide 19: Predicted Results vs Experimental Results
  Predicted Results
    South Farm & North Farm would be significantly quieter than Walker Roof
  Experimental Results
    The difference between South Farm and Walker Roof is negligible.
  Explanation
    Buildings block a large portion of anticipated RF interference

## Slide 20: Comparing and Ranking Test Sites
Category | Weight | Walker Roof | Pump House | South Farm | Patterson Lab | North Farm
Noise Floor | 3 | 1 | 3 | 5 | 2 | 4
Accessibility | 3 | 5 | 3 | 2 | 4 | 1
Internet | 2 | 5 | 3 | 2 | 4 | 1
Power | 2 | 5 | 3 | 4 | 2 | 1
Line of Sight | 2 | 4 | 2 | 5 | 1 | 3
Space | 1 | 5 | 1 | 4 | 2 | 3
Obstructions | 1 | 4 | 2 | 5 | 1 | 3
Terrian | 1 | 2 | 4 | 1 | 5 | 3
Elevation | 1 | 5 | 2 | 4 | 1 | 3
Weighted Totals |  | 62 | 49 | 54 | 40 | 35

## Slide 21: Conclusions and Next Steps
Permanent Ground Station on Walker Rooftop
  South Farm back-up location
Present findings to Mississippi State University and the MSU Aerospace Department
Repeatable Experiment Procedure
  University Student Groups
  Radio Enthusiasts

## Slide 22: Acknowledgements
CubeSat at MSU Student Team
Faculty Advisor, Mr. Wolz
MSU Aerospace Engineering Department
Bagley College of Engineering
American Institute of Aeronautics and Astronautics

## Slide 23
Questions?