## Slide 1
Marina R. Jenkins, Ryan B. Murdoch
University of Florida
AIAA Region II Student Conference, April 3-4, 2025
Copyright © by Marina R. Jenkins, Ryan B. Murdoch Published by the American Institute of Aeronautics and Astronautics, Inc., with permission.
Optimizing Fuel in Commercial Supersonic Flight

## Slide 2: Introduction
Resurgence of Supersonic Commercial Transport
  Similar to the Concorde
  Flying Faster
  Traveling Farther
  Without the threat of sonic booms
A problem still remains…
[1]

## Slide 3: Introduction
The traditional approach to fuel is flawed
  Fuel must have high energy density, economically sounds, stable.
  The jets must be lightweight enough to travel long distances at a high speed and large enough to carry a passenger load- while balancing economics and sustainability parameters.

## Slide 4: Background
Global SST Programs
  Tu-144
U.S SST development
  Funding cut 1971
Creation of the Concorde
  Air France/ British Airways

## Slide 5: Background
Sonic boom legislation
  1973
Eventual end of the Concorde program
  2003
New companies/Research
  Hermes
  Boom Supersonic

## Slide 6: Motivation
Efficiency, Accessibility, and Safety
In order to succeed in regard to these goals, fuel use must be optimized
[2]
‌

## Slide 7: Problems
  We optimized fuel via the following parameters:
    Cost
    Storage
    Aircraft Payload
    Environmental impacts
    Health Effects
  These parameters were broken into Production and Consumption stages

## Slide 8: Fuel Types
We selected the following fuel types:
Kerosene based fuels
  Jet-A
  JP-8
Sustainable Aviation Fuels (SAFs)
Hydrogen

## Slide 9: Kerosene Based Fuels
Refined from crude oil then distilled.
Jet-A
  Most common jet fuel
JP-8
  Standard for military use
These act as a control due to the history of their use.

## Slide 10: Fuel Types
SAFs
  Derived from renewable resources
  Typically used as a 50% blend with kerosene based fuels
  HEFA, ATJ, etc. production technologies
[3]

## Slide 11: Fuel Types
Hydrogen
  Hydrogen internal combustion engines (H2ICE) burn hydrogen in gas-turbine engines
  High energy density
  Low volumetric density
  Produced through multiple methods with varying CO2 outputs.
  Hydrogen Fuel Cells Convert hydrogen and oxygen into electricity
[4]

## Slide 12: Methods
The fuel performance was evaluated within each parameter, split between production and consumption.
We produced a matrix depicting their performances

## Slide 13: Methods: Sustainability
  Evaluated by magnitude of carbon emissions
    grams per megajoule of fuel
  Determines:
    Environmental impacts in producing and consuming the fuel

## Slide 14: Methods: Ease of Storage
Safe storage temperature range, (Celsius)
Range determined by the flash and freeze point
Hydrogen is assumed to be kept at its liquid state

## Slide 15: Methods: Specific Cost
Comparing the price of these fuels is difficult!
-Hydrogen
Cost USD per megajoule of energy
These units allow for a comparison of fuels of different characteristics

## Slide 16: Methods: Health Impacts
Production Stage: Minimal Risk Level
  Inhalation toxicity
Consumption Stage: Particulate Attributed Premature Deaths
  Nitrogen Dioxide(s) (Nox) attributed premature mortalities
  Nox attributes to 91% of premature deaths from particulate emmisions

## Slide 17: Methods: Payload Capabilities
Determined by:
Density (kg/L)
Gravimetric Energy Density (MJ/kg)
Volumetric Energy Density (MJ/L)
All three must be proportional enough to sustain supersonic flight

## Slide 18: Production Results

## Slide 19: Production Results: Ease of Storage
  SAFs are similar to Kerosene based fuels
    Interchangeability
  Hydrogen is difficult to store
    Requires cryogenic temperatures

## Slide 20: Production Results: Specific Cost
  Kerosene based fuels are the cheapest
    Crude Oil refining produces many fuel types driving the price of fuels down.
    Jet A (42.2), JP-8 (43.84)
  Hydrogen varies (25 -59)
  SAFs are expensive (70.4)

## Slide 21: Production Results: Sustainability
Due to the generalization of SAFs and Hydrogen fuels, minimum possible emissions was used
  SAFs and Hydrogen perform better than kerosene-based fuel
  (17 g/MJ)
  Depending on production methods both can emit no carbon emissions

## Slide 22: Production Results: Health Effects
  Minimal risk levels:
  Kerosene Based Fuels: 2.5 average
  SAFs: lower relative to kerosene based
  Hydrogen: no minimal risk level/nontoxic

## Slide 23: Consumption Results

## Slide 24: Consumption Results: Payload Capabilities
SAFs are very similar to Kerosene based fuels in terms of VED, GED, and ED (around 30-40 for each)
Gravimetrically hydrogen contains a high energy density (120)
  Hydrogens volumetric density is extremely low (8.5)
Unique density parameters result in…?

## Slide 25: Consumption Results: Health Effects
  Little to no difference in NOx emissions between Kerosene based and SAFs
  Hydrogen powered aircraft can contribute to a 86% reduction in Nox levels
  Due to SST flight elevation, their particulate emissions impact ozone and climate

## Slide 26: Consumption Results: Sustainability
  Kerosene based fuels and SAFs have significant Carbon emissions in consumption (73 g/MJ)
  Hydrogen emits no Carbon emissions

## Slide 27: Limitations
  Cost collection,
    Variable, unreliable
  Broadness of SAF creation
    Methods and implementations

## Slide 28: Conclusion
  Metric for synthesizing the optimization of SST fuels
    Applicable for non-SST
  No singular best fuel
    Willingness of companies to balance
    Sustainability and economics
    Mix of multiple fuel types
[5]

## Slide 29: References
[1]“Boom Supersonic and Collins Aerospace Sign Expanded Agreement for Major Aircraft Systems for Overture,” ‎@CollinsAero, 2025. https://www.collinsaerospace.com/news/news/2022/07/boom-supersonic-collins-aerospace-sign-expanded-agreement-for-major-aircraft-systems-overture (accessed Apr. 03, 2025).
[2] D. Dinius, “Supersonic Technologies - NASA,” NASA, Dec. 07, 2021. https://www.nasa.gov/centers-and-facilities/armstrong/supersonic-technologies/
[3] “Taking Off Soon: A New Kind of Sustainable Aviation Fuel (SAF),” www.honeywell.com. https://www.honeywell.com/us/en/news/2021/09/taking-off-soon-a-new-kind-of-sustainable-aviation-fuel-saf
[4] “Storing hydrogen fuel in salts — a step toward ‘cleaner’ energy production,” American Chemical Society. https://www.acs.org/pressroom/newsreleases/2022/october/storing-hydrogen-fuel-in-salts.html
[5] S. Hull, “What to do when babies cry on a plane - The Points Guy,” The Points Guy, Jun. 15, 2023. https://thepointsguy.com/airline/travel-etiquette-when-babies-cry-on-planes/ (accessed Apr. 03, 2025).
‌
‌