## Slide 1
3D Terrain Mapping and Optimal Path Planning for Autonomous Ground Vehicles in Off-road Environments
Matt Nguyen

## Slide 2
Introduction & Motivation
Autonomous ground vehicles (AGVs) are extensively employed in exploration tasks, such as planetary surface analysis, mine detection, and other remote environments.
This research aims to enhance AGV performance by improving the efficiency of mapping and path planning for optimal navigation.
Photo: issnationallab.org
Photo: clearpathrobotics.com

## Slide 3
Currently, the robot generates 2D maps from sensor data. Our goal is to develop 3D mapping and integrate path planning, allowing the robot to dynamically adjust its route based on its past and future predictions.
Problem formulation

## Slide 4
The problem of finding the optimal path consists of two main challenges:
          3D Terrain Modeling:
            Convert raw data into a 3D model terrain.
            Minimize deployment time, computational and data storage.
            Ensure interpolation of the original path into an area map while maintaining sufficient detail about terrain characteristics.
          Pathfinding Algorithm Selection:
            Develop an efficient sampling approach to generate nodes along the map.
            Identify a pathfinding algorithm that provides fast and accurate solutions.
            Ensure the algorithm efficiently determines the optimal route from the start to the goal nodes.
Approach Overview

## Slide 5
Data collection
High-accuracy clock module for GPS precision timing
Clear path Jackal AGV
Google satellite image of the terrain for which experimental tests were conducted

## Slide 6
Terrain mapping
Delaunay triangulation
Barycentric Coordinate
Lagrange Interpolation for multidimensions
The overview steps
Original scatter point graph of the GPS coordinate

## Slide 7
Terrain mapping
Given We want to get to a triangulation of vertex set with no edge can be added without crossing.1
Delaunay triangulation

## Slide 8
Terrain mapping
The barycentric weights () is calculated by the inverse of distances
Lagrange Interpolation will handle the depth of the map

## Slide 9
Result map
The terrain the robot was deployed on
Interpolated 3D map from the original path

## Slide 10
Sampling approaches
Randomly sampling approach
Grided sampling approach

## Slide 11
Cost Function
C(.) is the actual cost associated with the edges between vertices
is the difference in height.
is the parameter that reflects energy’s importance in our optimal path.
is the norm of the vector between notes or

## Slide 12
Path planning algorithm
A star algorithm illustration
A star employs Cost and Heuristic variables to find the optimal path:
      Cost is the total cost to get to a specific note.
          Heuristic how far it is in 2D using the distance function to figure out

## Slide 13
Results
Performance comparison of the two sampling approaches
Random sampling performance results
Gridded sampling performance results

## Slide 14
Results
Pathfinding result for 2D distance
Pathfinding results with 3D energy optimal

## Slide 15
Conclusion and Future work
  Future work will involve integrating additional sensors like IMU and LiDAR to improve map accuracy. The goal is for the robot to autonomously perform mapping and path-planning in real-time.
  Conclusion: The optimized data reduction enables 3D terrain mapping for the robot, enhancing efficiency and lengthening battery life.

## Slide 16
Thank you for listening

## Slide 17
References
Kindermann, Philipp. "Lecture 08: Delaunay Triangulation Part I: Height Interpolation." YouTube, uploaded by Philipp Kindermann, 26 June 2020, https://www.youtube.com/watch?v=6UsdvbiJx54.
Berrut, J.-P., and Trefethen, L. N., “Barycentric Lagrange Interpolation,” SIAM Review, Vol. 46, No. 3, 2004, pp. 501–517.https://doi.org/10.1137/S0036144502417715.
Klein, Georges. "Applications of linear barycentric rational interpolation." (2012). https://folia.unifr.ch/documents/302781/files/KleinG.pdf