## Slide 1
Nathan D. Kim, Sanchir Erdenebat, Kyle Law
Propulsive Landers at Georgia Tech
2025 Region II Student Conference, 3-4th April
Copyright © by Propulsive Landers, Georgia Institute of Technology. Published by the American Institute of Aeronautics and Astronautics, Inc., with permission.
Spline-Based Flight Path Planning and Following for Aerial Navigation

## Slide 2
How to get from point “A” to point “B”
Physical limitations change what is “feasible”
In the context of a 50 meter vertical hop
  External forces can cause deviations in our desired path
Works as a corrective algorithm
Motivation for path planning

## Slide 3
Constraints
  Maximum thrust
  Minimum thrust
  Maximum velocity
  Current state
  Maximum tilt
Limitations

## Slide 4
3rd degree interpolation
Smooth and continuous
Requires:
  Starting position (p0)
  Ending position (p1)
  Starting tangent (v0)
  Ending tangent (v1)
Hermite splines
H(t) = p0*(2t3-3t2+1)
+ v0*(t3-2t2+t)
+ p1*(-2t3+3t2)
+ v1*(t3-t2)

## Slide 5
3rd degree interpolation
Smooth and continuous
Requires:
  Starting position (p0)
  1st control point (c0)
  2nd control point (c1)
  Ending position (p1)
Bézier splines
B(t) = p0*(1-t)3
+ c0*3t(1-t)2
+ c1*3t2(1-t)
+ p1*t3

## Slide 6
Hermite splines account for initial conditions
Hermite splines requires 8 terms raised to a power, Bézier splines require 4
Can get an equivalent Bézier curve with:
  c0=p0+(⅓)v0
  c1=(p1x, p1y, p0z)+(⅔)(0, 0, p1z-p0z)
Create 100 points along the curve
Combining the two

## Slide 7
Each point represents a potential target point
Find closest valid target:
  𝜃 ≤ maximum tilt
  Not below us
When do we define a new path?
Target point
𝜃

## Slide 8
End with hovering
  Only target p1
Ignore 𝜃 constraint
Define “safety zone”
  Too little room for error can lead to infinite loops
Only redefine path if:
  Safety zone was left
  𝜃 > maximum tilt
End of path behavior
“Safety Zone”

## Slide 9
Combine benefits of Hermite and Bézier splines
Iteratively validate target points
Define endpoint behavior
Conclusion

## Slide 10
Validate the robustness and reliability through simulations then real flight
Future direction

## Slide 11
We would like to thank Anyi X. Lin, our subteam lead, for his initial findings and continued mentorship
We would also like to express our gratitude to Szu H. Chen, our project lead, and Propulsive Landers at Georgia Tech for allowing us the opportunity to conduct research as a team
Acknowledgements