## Slide 1
Nicholas Pisani, Peter Waszkowski
Florida Institute of Technology
AIAA Student Conference Region II, April 3 & 4, 2025
Copyright © by Nicholas Pisani & Peter Waszkowski, Florida Institute of Technology Published by the American Institute of Aeronautics and Astronautics, Inc., with permission.
A Review of Hypersonic Vehicle Engine Optimization

## Slide 2: Background on Hypersonics
Future of government and civilian aircraft
Utilize supersonic combustion to provide sufficient thrust
In the past, have not been independently operated: Rockets or supersonic aircraft
[16]

## Slide 3: Introduction
Hypersonic vehicles have the potential to improve both government and civilian aerospace capabilities:
Stealth, response time and survivability
Thrill seeking and high-speed travel
Reusable launch vehicles

## Slide 4: Introduction
Inlets
Combustion Stabilization
Nozzles
Combined Cycle

## Slide 5: Following the Flow Path
Inlets
Combustion Stabilization
Nozzles
Combined Cycle
Notes: Inlets = streamline shock inducing geometry through variable geometry and integration within combined cycle engines
Nozzle = Rao’s method/proper design analysis to increase efficiency and limit trailing edge flow interaction

## Slide 6: Background on Inlets
Primary purpose of inlets in hypersonic vehicle engines is to decelerate and pressurize flow
Main scramjet inlet inefficiencies: Spillage drag and shock losses
[17]

## Slide 7: Inlets: Ramjet compression system
Straight cowl lip inlet used for a ramjet and scramjet combined inlet section
[5]
[5]

## Slide 8: Inlets: Ramjet compression system
Drawbacks of Configuration 1:
Shock angle interference
Less aerodynamic profile
Insufficient thrust values
Mach #
[5]
Configuration 1:

## Slide 9: Inlets: Ramjet compression system
Solution: Configuration 2
Benefit:
Eliminate shock angle interference
More aerodynamic profile
Configuration 1
Configuration 2:
Mach #
[5]
[5]

## Slide 10: Inlets: Ramjet compression system
Inlet design proved successful for the ramjet, but not the scramjet at hypersonic flight regimes
Pressure Recovery Factor (PRF): Quantity used to characterize an inlet’s ability to recover pressure levels after shock interactions
[5]
Inlet Efficiency: Direct relationship with PRF
[5]

## Slide 11: Inlets: Benefits of variable geometry
Performance analysis of cowl motions using a low-order model designed for control-oriented applications that simulate wave interactions [6].
Forward/backward
Three Cowl Lip Motions:
2) Up/Down
3) Rotation
[6]
[6]
[6]

## Slide 12: Benefits of variable inlet geometry:
Two main categories of results analysis indicate benefit of vertical displacement (up and down motion):
      PRF
  Capture Area
[6]
[6]

## Slide 13: Following the Flow Path
Inlets
Combustion Stabilization
Nozzles
Combined Cycle

## Slide 14: Combustion Stabilization: Background
Constant, predictable thrust
Mixing, residence, reaction
Cavity flame holding
Plasma enhancement
Shock induced combustion
[3]
Notes: Flow mixing time increases the combustion ability
elongating flow residence time allows the stabilization
improves the ability to stay within the combustion chamber

## Slide 15: Combustion Stabilization: Flameholding
Fuel jet and cavity  Mixing enhancement
Plasma Injection Module  Reaction enhancement
[7]
[8]
Notes: Fuel jet and cavity - location and shape of shear layer interaction will influence shape of flame -> affecting the distribution and propagation; High-pressure injector = further upstream combustion; low-pressure injector = potential to fully ignite downstream of cavity
Fuel jet/cavity -> flame spreading angle increases cause increase in combustion process, mixing, propagation, and chem rxn time; too much causes aggressive disruption in boundary layer and choking effect
PIM -> higher normalized pressures at high fuel mass flow rates can be used (rich) & viscous cycle of discharge/ignition/no discharge/no ignition (varying pressures)

## Slide 16: Combustion Stabilization: Ignition
Oblique shock ignition
2 modes:
  Inviscid flow combustion
  Separation zone combustion
[10]
Notes: inviscid flow field -> peak heat load occurring downstream of separation zone created; lower local heat loads
separation zone -> amplifies boundary layer separation zone and increases local heat loads; thermal failure
Must be high stagnation temp (not low/sub sonic) and uniform distribution of flow

## Slide 17: Following the Flow Path
Inlets
Combustion Stabilization
Nozzles
Combined Cycle
Notes: Inlets = streamline shock inducing geometry through variable geometry and integration within combined cycle engines
Nozzle = Rao’s method/proper design analysis to increase efficiency and limit trailing edge flow interaction

## Slide 18: Background on Nozzles
Goal of nozzles: depressurize and accelerate flow
Influence interactions between exhaust flow and bypass flow - cannot cause drag
Flow cannot be underexpanded nor overexpanded
[17]

## Slide 19: Nozzles: Effective hypersonic designs
Testing the effectiveness of three existing hypersonic nozzles based on surface area and nozzle geometry:
SOLIDWORKS Model of de Laval Nozzle
Bell Nozzle
Dual-Bell Nozzle
[11]
**de Laval and Bell shortened using Rao’s Method
*Note: not the design from this study
DB Base
DB Extension
[16]
de Laval Nozzle

## Slide 20: Nozzles: Effective hypersonic designs
Quantitative results of simulation and analysis:
Rao’s Method: Maximize thrust while minimizing surface area
*Fuel chosen was Hydrogen gas: real scramjet nozzle experience
[11]

## Slide 21: Nozzles: Hypersonic design process
Development of hypersonic nozzles is extensive and should focus mainly on four steps:
Control Volume Analysis
Force and force vector analysis
Rao’s Method
Method of Characteristics
Streamline Angle, deg
Mach #
Exhaust pressure
Ambient pressure
[2]

## Slide 22: Nozzles: Main Takeaways
Produce effective performance models
  Minimize surface area
  Determine effective nozzle contour
Efficient Nozzles Efficient Engines Efficient Vehicles
[18]

## Slide 23
Inlets
Combustion Stabilization
Nozzles
Combined Cycle
Following the Flow Path
Notes: Inlets = streamline shock inducing geometry through variable geometry and integration within combined cycle engines
Nozzle = Rao’s method/proper design analysis to increase efficiency and limit trailing edge flow interaction

## Slide 24: Background on Combined Cycle Engines
Full flight operation
Turbine-based (TBCC) vs. Rocket-based (RBCC)
The mode transition is a key point of interest
[4]
[4]

## Slide 25: Parallel TBCC
Two flow paths
More complex - requires additional mechanical systems
Aerodynamic forces during transition must be considered
[12]
Notes: Thrust coefficient of exhaust system over 0.9; sharp decrease in lift will cause strong aerodynamic moments to be corrected by flaps in transition.

## Slide 26: Tandem TBCC
Single flow path
Technology level
Transition between turbine and ramjet operation is difficult
[13]
Notes: net thrust variance of 4% and mass flow rate less than 8% variance; turbojet blown out -> decrease in mach number of inlet to the ramjet combustion area potentially causes ramjet unstart

## Slide 27: Conclusion
Prioritize overall engine efficiency by combining aspects
More research necessary
  Combination cycle engines
  Physical experimentation crucial
[19]
[19]

## Slide 28: References
[1] Ma, Y., Guo, M., Tian, Y., & Le, J. (2024). Recent advances and prospects in hypersonic inlet design and intelligent optimization. Aerospace Science and Technology, 146, 108953. https://doi.org/10.1016/j.ast.2024.108953
[2] Cain, T. (2010, September). Scramjet nozzles - DTIC. NATO Research and Technology Organization. https://apps.dtic.mil/sti/pdfs/ADA592961.pdf
[3] Qili Liu, Damiano Baccarella, Tonghun Lee, Review of combustion stabilization for hypersonic airbreathing propulsion, Progress in Aerospace Sciences, Volume 119, 2020, 100636, ISSN 0376-0421, https://doi.org/10.1016/j.paerosci.2020.100636. (https://www.sciencedirect.com/science/article/pii/S0376042120300488)
[4] McDaniel, J., Goyne, C., Edwards, J., Chelliah, H., Cutler, A., & Givi, P. (2009). US National Center for Hypersonic Combined Cycle Propulsion: An overview. 16th AIAA/DLR/DGLR International Space Planes and Hypersonic Systems and Technologies Conference. https://doi.org/10.2514/6.2009-7280
[5] Veeran, S., Pesyridis, A., & Ganippa, L. (2018). Ramjet compression system for a hypersonic air transportation vehicle combined cycle engine. Energies, 11(10), 2558. https://doi.org/10.3390/en11102558
[6] Dalle, D. J., Torrez, S. M., & Driscoll, J. F. (2011). Performance analysis of variable-geometry scramjet inlets using a low-order model. 47th AIAA/ASME/SAE/ASEE Joint Propulsion Conference & Exhibit. https://doi.org/10.2514/6.2011-5756
[7] A. Ben-Yakar, M.G. Mungal, R.K. Hanson, Time evolution and mixing characteristics of hydrogen and ethylene transverse jets in supersonic crossflows, Phys. Fluids. 18 (2006) 026101. https://doi.org/10.1063/1.2139684
[8] Wang, H., Wang, Z., Sun, M., & Qin, N. (2013). Combustion characteristics in a supersonic combustor with hydrogen injection upstream of Cavity Flameholder. Proceedings of the Combustion Institute, 34(2), 2073–2082. https://doi.org/10.1016/j.proci.2012.06.049
[9] Savelkin, K. V., Yarantsev, D. A., Adamovich, I. V., & Leonov, S. B. (2015). Ignition and Flameholding in a supersonic combustor by an electrical discharge combined with a fuel injector. Combustion and Flame, 162(3), 825–835. https://doi.org/10.1016/j.combustflame.2014.08.012
[10] Veraar, R., Mayer, A., Verreault, J., Stowe, R., Farinaccio, R., & Harris, P. (2009). Proof-of-principle experiment of a shock-induced combustion ramjet. 16th AIAA/DLR/DGLR International Space Planes and Hypersonic Systems and Technologies Conference. https://doi.org/10.2514/6.2009-7432
[11] Vianna Moizes, D. A., Kotler, A. R., Thornton, M. R., & Ahmed, K. A. (2023). Comparison and analysis of hypersonic scramjet nozzles. AIAA SCITECH 2023 Forum. https://doi.org/10.2514/6.2023-0716
[12] Li, C., Xu, J., Mo, J., & Zhang, K. (2009). Numerical simulation of the unsteady mode transition process of an over-under TBCC exhaust system. 45th AIAA/ASME/SAE/ASEE Joint Propulsion Conference &amp;Amp; Exhibit. https://doi.org/10.2514/6.2009-5301
[13] Zhang, M., Wang, Z., Liu, Z., & Zhang, X. (2016). Analysis of mode transition performance for a tandem TBCC engine. 52nd AIAA/SAE/ASEE Joint Propulsion Conference. https://doi.org/10.2514/6.2016-4573
[14] Russel, J. (2009). Turbine-based combined cycle propulsion. Turbine-Based Combined Cycle Propulsion. https://www.colorado.edu/faculty/kantha/sites/default/files/attached-files/russell.pdf

## Slide 29: Further Image References
[15] Kylie, N. (2024, December 16). SR-72: 5 advances expected in the hypersonic UAV “son of blackbird.” Simple Flying. https://simpleflying.com/5-advances-hypersonic-uav-son-of-blackbird/
[16] Génin, C., Schneider, D., & Stark, R. (2020). Dual-Bell nozzle design. Notes on Numerical Fluid Mechanics and Multidisciplinary Design, 395–406. https://doi.org/10.1007/978-3-030-53847-7_25
[17] University, T. (n.d.). Horizon Inlet Unstart Dynamics. Space Institute. https://www.utsi.edu/horizon/research/inlet-unstart-dynamics/
[18] Wikimedia Foundation. (2025, March 13). Jet engine. Wikipedia. https://en.wikipedia.org/wiki/Jet_engine#Nozzles
[19] Chimera. Hermeus. (n.d.). https://www.hermeus.com/chimera