## Slide 1
Ibrahim Arnous & Joseph Colangelo
Embry-Riddle Aeronautical University
2025 Region II Student Conference, 3 April 2025 – 4 April 2025
Distributed CubeSat Spectroscopy Network for Martian Surface and Atmospheric Analysis

## Slide 2: Mission Overview
The M-STAR mission deploys a constellation of 20 CubeSats into a polar sun-synchronous orbit around Mars, each equipped with either an ultraviolet-visible (UV-Vis) spectrometer or an infrared (IR) spectrometer.

## Slide 3: Mission Phases
Phase I
  Deployment of 20 CubeSats into 175 km polar sun-synchronous orbit
  Spectral mapping using UV-Vis (200–700 nm) and IR (0.7–10 μm) spectrometers
  Global coverage achieved in 3 days with 25 km-wide swath scans
X: Deployment of 20 CubeSats into 175 km polar sun-synchronous orbit

## Slide 4: Mission Phases
Phase II
  Orbit adjusted for prolonged atmospheric observations (~5-year mission)
  Monitoring dust storms, trace gases, temperature fluctuations
  CubeSats serve as data relays and weather trackers for future missions

## Slide 5: Mission Architecture
Platform: 20 CubeSats with modular UV-Vis or IR spectrometers
Orbit: 175 km polar sun-synchronous orbit
Instruments:
  UV-Vis (200–700 nm): Detects organics, volatiles
  IR (0.7–10 μm): Identifies minerals, hydrated materials
Key Tech:
  Chameleon SWIR camera for real-time dust/cloud tracking
  Tunable filters, beam splitters, and onboard calibration
  X-band / Ka-band comms via relay or direct-to-Earth
Power: Solar + battery system, 40 W per CubeSat

## Slide 6: Mission Timeline

## Slide 7: Technical Diagram

## Slide 8: 3D Model

## Slide 9: Scientific Motivation
Expand spectral coverage with dual-wavelength sensing
Improve spatial and temporal coverage
Long-term climate and atmospheric studies
Demonstrate scalable, low-cost science architecture
Enable safer, more informed Human exploration

## Slide 10: Ultraviolet-Visible Spectrometer System
High sensitivity to organic compounds, detect potential biosignatures
Trace volatiles and surface-atmosphere interactions
Map Oxidized Minerals Indicative of Past Water
Monitor Atmospheric Composition and Climate Dynamics
Support Human Exploration and ISRU

## Slide 11: Infrared Spectrometer System
Wavelength Range: 0.7–10 micrometers (μm), covering the near to mid-infrared spectrum.
Identify Minerals: Detects mineral compositions (e.g., silicates, carbonates, sulfates) via their characteristic absorption bands within the 0.7–10 μm range.
Detect Hydrated Materials: Identifies water-bearing compounds
Monitor Atmospheric Composition, Water Vapor, Carbon Dioxide, Methane

## Slide 12: Dual spectrometer coverage

## Slide 13: Dual Spectrometer Technology
ALICE (New Horizons): UV-Vis for volatiles
TES (Mars Global Surveyor): IR for minerals
CRISM (Mars Reconnaissance Orbiter): Dual-range mapping
IUVS (MAVEN): UV-Vis for atmosphere
PFS (Mars Express): IR for atmospheric analysis

## Slide 14: Comparison with Previous Missions

## Slide 15: Distributed Network Advantages
  Enhanced spatial and temporal resolution
  Redundancy and mission resilience
  Simultaneous multi-point observations
  Scalable architecture
  Cost-effective approach (CubeSats)

## Slide 16: Dual Spectrometer Advantages
  Comprehensive spectral coverage
  Complementary detection capabilities
  Cross-validation between instruments
  Enhanced science return
  Support for multiple science objectives

## Slide 17: Scientific Impact

## Slide 18: Applications and Future Work
Support for Human Exploration
  Resource mapping
  Hazard assessment
  Landing site selection
  In-situ resource utilization (ISRU)
  Weather forecasting

## Slide 19: Applications and Future Work
Future Work
  Technology demonstration for future missions
  Adaptation for other planetary bodies
  Integration with other Mars missions
  Advanced data processing algorithms
  Machine learning for data analysis

## Slide 20: Website for more Information!!

## Slide 21
Questions?