## Slide 1
Amare Johnson, Madden Pierce, Maria Ivey
University of South Carolina
Region II Student Conference, 2025
Copyright © by Amare Johnson, Madden Pierce, and Maria Ivey Published by the American Institute of Aeronautics and Astronautics, Inc., with permission.
High-Altitude Balloon Satellite

## Slide 2: Design Team
Amare Johnson
Irmo, SC
Aerospace Engineering
Maria Ivey
York, SC
Aerospace Engineering
Madden Pierce
Turbeville, SC
Aerospace Engineering

## Slide 3: Assignment Details
UofSC Senior Design Project
Assignment: Design, manufacture, and test a high-altitude balloon system capable of reaching 30 km while capturing photos and transmitting real-time temperature and humidity data to the ground.
Commercially sourced
Recoverable, reusable
Comply with FAA, NFPA, and FCC

## Slide 4: Mission and Project Objective Statement
Project Objective Statement: “Develop and design a high-altitude balloon satellite system using a budget of $1250 within 3 months using commercially sourced products”
Mission Statement: “Deliver a recoverable data acquisition payload to the stratosphere (30km) and transmit telemetry data to a ground station”

## Slide 5: Conceptual Design Phase
Initial design improvements:
Crossbars to increase coupling between balloon neck and payload
Air scoops to dampen rotation

## Slide 6: Final Design Configuration
Double crossbar instead of parachute basket
Foam payload housing
  5 x 10 x 12 in
  Insulation
PVC crossbars
40 lb fishing line
Lightweight, simple to assemble
FAA §101.35

## Slide 7: Balloon and Parachute Selection
Parachute: 3 ft diameter
Weight: 2.4 oz
Descent rate: < 25 ft/s
1500 g balloon
Burst Altitude: 35 – 40 km

## Slide 8: Helium Calculation
~ 28 grams of lift/cu. ft. of helium
For a 1500 g balloon:
< 4 lb payload
Target ascent rate: 5.8 m/s
Total ascent time: ~ 87 min
191 cubic ft. of helium
NFPA 55
“Balloon Performance Calculator Tutorial” High Altitude Science

## Slide 9: Flight Path Predictability
Launch from Spartanburg, SC
Launch from Camden, SC
FAA §101.37
“Predicting the Flight Path” Stratoflights

## Slide 10: Computer System
Single-board computer
GPS receiver
Radio transmitter
APRS functionality

## Slide 11: Imaging
AKASO V50X Action Camera
HD video – 720p for 180 min
Internal battery
Raspberry Pi Camera Module
1080p
AKASO V50X
V2-8 Camera Module

## Slide 12: Communications
434 MHz transmitter, APRS
Ground station operating range: 400 – 460 MHz
Local tracking – 200 ft
Raspberry Pi Zero W
APRS
GPS Stubby Antenna
RG174 Tail Antenna
Tile tracker
FCC§97.5, §FAA 101.9

## Slide 13: Data Acquisition
Temperature/humidity
  Operating range: -40 to 80 °C
  Accuracy of +/- 2% RH and +/- 0.5 °C
CO2
  Accuracy of +/- 3%
DHT22
Senseair K30

## Slide 14: Power System
Four lithium AA batteries
3.6 V per battery
Operating temp -55 to 85 °C
~ 11 hours operating time

## Slide 15: Expected Layout

## Slide 16: Weight Breakdown
< 4 lb payload complies with FAR §101.1

## Slide 17: Budget Breakdown
$1250 budget

## Slide 18: Possible Improvements
Solar panels for additional power
Higher freq. transmission
Hydrogen for lower cost
Higher quality hardware
Carbon fiber structure
Aerodynamic payload housing

## Slide 19: APPLICATIONS
Climate research
Weather forecasting
Disaster monitoring